## Slide 1
SWISS SIA COMPLIANCE CHECKER
Turning IESVE models into evidence-based SIA readiness reports
Progress review for Friday oral presentation
SIA 380/2:2022
SIA 4010:2023
IESVE API
Current project: ZOER_32_C1
01
Notes: Open by framing the project as an evidence workflow, not just a Python script.
Mention that the deck is in English and intended for manager-level progress review.

## Slide 2
EXECUTIVE MESSAGE
We moved from ad hoc review to a repeatable readiness workflow
The project now extracts VE data, checks what can be checked, and blocks unsafe compliance claims where evidence is missing.
Swiss SIA Compliance Checker for IESVE
02
Run button
Workflow constraint solved
Designed for VE users who cannot run PowerShell.
26 sheets
Professional Excel output
Dashboard, action board, evidence tabs and raw traceability.
169 checks
Release validation
PDF references, config guardrails, workbook structure and formula health.
Core principle
No evidence,
no claim.
Notes: This is the main executive message.
The workflow is useful now because it is conservative and auditable.

## Slide 3
WHY IT MATTERS
Swiss compliance needs more than a pass/fail script
The standards create three simultaneous challenges: technical extraction, source traceability, and official evidence boundaries.
Swiss SIA Compliance Checker for IESVE
03
CHALLENGE
1
SIA 380/2 mixes building data, systems, controls and dynamic results.
2
SIA 4010 validates method/software evidence, not a single building value.
3
VE exposes data through specific IESVE API objects and CDB methods.
The required shift
From checking isolated numbers to proving where each value came from, how it was interpreted, and what remains not checkable.
Notes: Explain why this is difficult and why a professional report needs evidence boundaries.
Avoid claiming certification. The tool creates readiness and audit support.

## Slide 4
WHAT WE BUILT
The current architecture links VE extraction to manager-ready reporting
Each stage is designed to be auditable and safe to run inside VE.
Swiss SIA Compliance Checker for IESVE
04
1
VE Run button
User launches inside IESVE
2
IESVE API
Rooms, surfaces, CDB, Vista
3
SIA checks
380/2 values and model QA
4
Evidence matrix
4010 remains NOT_CHECKABLE
5
Reports/docs
Excel, Sphinx, playbooks
Notes: Walk left to right.
Stress that the tool is run-button compatible and uses IESVE-specific APIs.

## Slide 5
WHAT IS DELIVERED
The report has become an action system, not just a spreadsheet
The workbook now separates executive decisions, technical findings, evidence needs and raw traceability.
Swiss SIA Compliance Checker for IESVE
05
Executive view
MANAGER DASHBOARD
CLIENT SUMMARY
PREFLIGHT
Action board
P1 REMEDIATION
INPUT REQUEST
OPEN ITEMS BACKLOG
Technical audits
FRAME FRACTION AUDIT
ENVELOPE U REVIEW
VE G-VALUES AUDIT
Evidence guardrails
SIA4010 READINESS
SOFTWARE REGISTER
NAVIGATOR BACKLOG
Notes: This slide shows what has been built in concrete terms.
Mention that the report is built for managers, model reviewers and compliance reviewers at the same time.

## Slide 6
LATEST MODEL RESULT
ZOER_32_C1 is measurable, but not ready for a final compliance claim
The current run is useful because it makes the remaining work explicit.
Swiss SIA Compliance Checker for IESVE
06
65.8
Model QA
45.6
SIA 380/2 score
2/5
SIA 4010 evidence
4
Rooms
392.5
Area m2
Decision today: keep this as a professional readiness report, not a final SIA compliance certificate.
Notes: Use this slide to be transparent. The report is valuable because it shows exactly what is not ready.
Avoid over-selling the result.

## Slide 7
KEY TECHNICAL BREAKTHROUGH
The g-value issue is now evidence-backed
The script no longer treats CDB g_value = 0.75 as the SIA-comparable value when bs_en_410 proves otherwise.
Swiss SIA Compliance Checker for IESVE
07
Construction
CDB g
EN 410
Status
STD_EXTW
0.750
0.251
Pass
STD_EXT1
0.750
0.480
Pass
STD_EXT2
0.750
0.250
Pass
Why this matters
The report can now prove that raw CDB g-value and EN 410 g_perp are different values.
Result: no false g_total blocker when EN 410 already satisfies g <= 0.50.
Notes: This is a strong technical success.
Mention VECdbConstruction.get_g_values().bs_en_410 as the IESVE API evidence route.

## Slide 8
REMAINING SIA 380/2 BLOCKERS
The remaining model blockers are concrete and fixable
They are no longer vague compliance risks: they are specific constructions with exact values.
Swiss SIA Compliance Checker for IESVE
08
Chart: 
| STD_EXTW | STD_EXT2 | STD_EXT1
Frame fraction | 0.3 | 0.35 | 0.25
Limit | 0.25 | 0.25 | 0.25
Frame fraction
STD_EXTW = 0.30 and STD_EXT2 = 0.35 are above the retained 0.25 readiness value.
External wall U-value
STD_EXT1, STD_PAR1, STD_WAL2 = 0.222 W/(m2K), above the retained 0.20 limit.
Notes: The point is that the remaining blockers are manageable.
They need VE/CDB correction or auditable justification, not script guessing.

## Slide 9
SIA 4010 BOUNDARY
SIA 4010 remains blocked by official evidence, by design
The workflow is conservative: it tracks readiness, but it does not claim software validation without official files.
Swiss SIA Compliance Checker for IESVE
09
Evidence families
2 of 5
Current evidence coverage
40%
Missing before any validation wording
Official SIA test specifications
Official evaluation workbooks
Reference comparisons and class confirmation
Also: the manager-provided register does not list IESVE as software-level validated.
Notes: This is a safeguard slide.
Explain that SIA 4010 needs official evidence and target class confirmation.

## Slide 10
ROADMAP
The MVP is working; the MSP needs evidence automation and reviewer workflows
The next phase should focus on converting open items into repeatable evidence packages.
Swiss SIA Compliance Checker for IESVE
10
1
Now
Fix current VE model blockers
Frame fraction, wall U-value, next report validation
2
Next
Add justified-by-evidence status
Keep true values visible while allowing signed exceptions
3
MSP
Automate broader evidence pack
Schedules, ventilation, HVAC efficiency, SIA 4010 class files
Definition of done
A model can be discussed confidently when every pass, fail and exception has a visible source.
Notes: Use this as the path forward.
MVP works. MSP means commercial-quality evidence and reviewer workflow.

## Slide 11
DECISION AND ASK
The next milestone is a corrected model plus official evidence plan
With the current tooling in place, the work can now move from scripting to controlled compliance review.
Swiss SIA Compliance Checker for IESVE
11
Ask 1
Approve model remediation on frame fraction and wall U-value.
Ask 2
Confirm the target SIA 4010 validation class and required official files.
Ask 3
Use the next VE Run as the go/no-go checkpoint for MVP handoff.
Proposed close: the project is no longer exploratory. It is ready for structured remediation and evidence collection.
Notes: End with specific asks, not a generic thank-you.
If time allows, invite questions on remediation priority or SIA 4010 evidence ownership.